For our other two free eBooks,
 Go to: 1 - 100 Transistor Circuits
 Go to: 101 - 200 Transistor Circuits

For more data on the 555, see these pages:

555-Page 1    for CD users:   555-Page 1
555-Page 2                                555-Page 2  
555-Page 3                                555-Page 3  
555-Test                                     555-Test

Save 50 - 555 Circuits (actually 59 Circuits) as:  zip (460kB) or  .doc (790kB) or .pdf (500kB)

54 CIRCUITS as of  29-11-2009       Rev1.2 29-11-2009 - added Hysteresis (Schmitt Trigger), Knight Rider-2, Morse Code,
Music Box,  Reaction Timer Game

59 CIRCUITS as of  30-11-2009       Rev1.3 30-11-2009 - added Traffic Lights, Driving White LEDs, TV Remote Control Jammer,
3x3x3 Cube, Up/Down Fading LED

See TALKING ELECTRONICS WEBSITE

                                           email Colin Mitchell:   talking@tpg.com.au

INTRODUCTION This e-book covers the 555. The 555 is everywhere and it is one of the cheapest and most-rugged chips on the market. It comes as a TTL 555 and will operate from 5v to about 16-18v. It costs from 20 cents (eBay) to $1.20 depending on the quantity and distributor. The circuitry inside the chip takes about 10mA - even when the output is not driving a load. This means it is not suitable for battery operation if the chip is to be powered ALL THE TIME. The 555 is also available as a CMOS chip (ICM7555 or ICL7555 or TLC555) and will operate from 2v to 18v and takes 60uA when the circuitry inside the chip is powered. The "7555" costs from 60 cents (eBay) to $2.00 We call the TTL version "555" and the CMOS version "7555." This is called ELECTRONICS JARGON. The 555 comes as a single timer in an 8-pin package or a dual timer (556) in a 14 pin package. The 7555 comes as a single timer in an 8-pin package or a dual timer (7556) in a 14 pin package. The 555 and 7555 are called TIMERS or Timer Chips. They contain about 28 transistors and the only extra components you need are called the TIMING COMPONENTS. This is an external resistor and capacitor. When a capacitor is connected to a voltage, it take a period of time to charge. If a resistor is placed in series with the capacitor, the timing will increase. The chip detects the rising and falling voltage on the capacitor. When the voltage on the capacitor is 2/3 of the supply the output goes LOW and when the voltage falls to 1/3, the output goes HIGH. We can also do other things with the chip such as "freezing" or halting its operation, or allowing it to produce a single HIGH-LOW on the output pin. This is called a "ONE-SHOT" or MONOSTABLE OPERATION. When the chip produces an output frequency above 1 cycle per second, (1Hz), the circuit is called an OSCILLATOR and when below one cycle per second, it is called a TIMER. Colin Mitchell TALKING ELECTRONICS. talking@tpg.com.au To save space we have not provided lengthy explanations of how any of the circuits work. This has already been covered in TALKING ELECTRONICS Basic Electronics Course, and can be obtained on a CD for $10.00 (posted to anywhere in the world) See Talking Electronics website (http://www.talkingelectronics.com) for more details on the 555 by clicking on the following four pages: 555-Page 1 555-Page 2 555-Page 3 555-Test Many of the circuits have been designed by Colin Mitchell Music Box, Reaction Timer Game, Traffic Lights, TV Remote Control Jammer, 3x3x3 Cube, while others are freely available on the web. But this eBook has brought everything together and covers just about every novel 555 circuit. If you think you know everything about the 555, take the 555-Test and you will be surprised! How are your powers of observation? Can you find the LED: SQUARE WAVE OSCILLATOR KIT A Square Wave Oscillator Kit is available from Talking Electronics for under $10.00 Buy a kit (This link will send an email to Colin Mitchell and you will be advised of costs and how to send money via Paypal or credit card.) Or email Colin Mitchell: talking@tpg.com.au 555 KIT Buy 555 kit A kit of components to make many of the circuits described in this eBook is available for $10.00 plus $7.00 post. The kit contains the following components: 2 - 220R 2 - 1k 2 - 4k7 2 - 10k 2 - 33k 2- 100k 2 - 1M 1 - 10k mini pot 1 - 100k mini pot 2 - 10n 2 - 100n 1 - 10u electrolytic 1- 100u electrolytic 2 - 1N4148 signal diodes 2 - BC547 transistors 1 - BC557 transistor 1 - 555 timer chip 1 - 8 pin IC socket 1 - red LED 1 - green LED 1 - orange LED 1 - mini 8R speaker 1 - mini piezo 1 - LDR (Light Dependent Resistor) 1 - 10mH inductor 1 - push button 1 - tactile push button 1 - Experimenter Board (will take 8, 14 and 16 pin chips)

CONTENTS Active High Trigger Active Low Trigger Amplifier using 555 Astable Multivibrator Bi-Coloured LED Bi-Polar LED Driver Building the Circuits Car Tachometer Clark Zapper Clicks Uneven Continuity Tester Dark Detector Driving A Bi-Coloured LED Driving A Relay Driving White LEDs Flashing Indicators Flashing Railroad Lights Flip Flop Function of each 555 pin Hee Haw Siren High Frequency 555 Oscillator How to use the 555 Hysteresis Increasing Output Current Increasing Output Push-Pull Current Inverter 12v to 240v Inside the 555 Kitt Scanner Knight Rider Laser Ray Sound Latch LED Dimmer Light Controlled Screamer Siren Light Detector Low Frequency 555 Oscillator Machine Gun Memory Cell Metal Detector Monostable 555 Morse Keyer Mosquito Repellent Motor PWM Multivibrator - Astable Music Box Negative Voltage Normally Closed Trigger One-Shot 555 Organ Police Siren Pulse Extender Pulser - 74c14 PWM Controller Railroad Lights (flashing) Rain Alarm Reaction Timer Game Replacing 556 with two 555's Resistor Colour Codes Schmitt Trigger Screamer Siren - Light Controlled Servo Tester Simplest 555 Oscillator Siren 100dB Square Wave Oscillator Stun Gun Substituting a 555 - Part 1 Substituting a 555 - Part 2 Switch Debounce Tachometer Ticking Bomb Tilt Switch Touch Switch Toy Organ Traffic Lights Transistor Tester Trigger Timer - 74c14 TV Remote Control Jammer Uneven Clicks Up/Down Fading LED Using the 555 Voltage Doubler Wailing Siren Zapper (Dr Clark) Zener Diode Tester 2 Minute Timer - 74c14 3x3x3 Cube 10 Minute Timer - 74c14 12v to 240v Inverter 100dB Siren 555 Amplifier 555 Kit of Components 555 Pinout 555 Mistakes (No-No's) 556 Dual Timer

to Index

THE 555 PINS Here is the identification for each pin: When drawing a circuit diagram, always draw the 555 as a building block, as shown below with the pins in the following locations. This will help you instantly recognise the function of each pin: Pin 1 GROUND. Connects to the 0v rail. Pin 2 TRIGGER. Detects 1/3 of rail voltage to make output HIGH. Pin 2 has control over pin 6. If pin 2 is LOW, and pin 6 LOW, output goes and stays HIGH. If pin 6 HIGH, and pin 2 goes LOW, output goes LOW while pin 2 LOW. Pin 3 OUTPUT. (Pins 3 and 7 are "in phase.") Pin 4 RESET. Internally connected HIGH via 100k. Must be taken below 0.8v to reset the chip. Pin 5 CONTROL. A voltage applied to this pin will vary the timing of the RC network. Pin 6 THRESHOLD. Detects 2/3 of rail voltage to make output LOW only if pin 2 is HIGH. Pin 7 DISCHARGE. Goes LOW when pin 6 detects 2/3 rail voltage but pin 2 must be HIGH. If pin 2 is HIGH, pin 6 can be HIGH or LOW and pin 7 remains LOW. Goes OPEN (HIGH) and stays HIGH when pin 2 detects 1/3 rail voltage (even as a LOW pulse) when pin 6 is LOW. (Pins 7 and 3 are "in phase.") Pin 7 is equal to pin 3 but pin 7 does not go high - it goes OPEN. Pin 8 SUPPLY. Connects to the positive rail.

to Index

THE SIMPLEST 555 OSCILLATOR The simplest 555 oscillator takes output pin 3 to capacitor C1 via resistor R1. When the chip is turned on, C1 is uncharged and output pin 3 is HIGH. C1 charges via R1 and when Pin 6 detects 2/3 rail voltage, output pin 3 goes LOW. R1 now discharges capacitor C1 and when pin 2 detects 1/3 rail voltage, output pin 3 goes HIGH to repeat the cycle.

to Index

INSIDE THE 555 Note: Pin 7 is "in phase" with output Pin 3 (both are low at the same time). Pin 7 "shorts" to 0v via a transistor. It is pulled HIGH via R1. Maximum supply voltage 16v - 18v Current consumption approx 10mA Output Current sink @5v = 5 - 50mA @15v = 50mA Output Current source @5v = 100mA @15v = 200mA Maximum operating frequency 300kHz - 500kHz Faults with Chip: Consumes about 10mA when sitting in circuit Output voltage can be up to 2.5v less than rail voltage Output can be 0.5v to 1.5v above ground Sources up to 200mA but sinks only 50mA NE555 tested at 1kHz, 12.75v rail and 39R load: Results: Output voltage 0.5v low, 11.5v high current = 180mA The "test chip" performance was excellent.

to Index

HOW TO USE THE 555 There are many ways to use the 555. They can be used in hundreds of different circuits to do all sorts of clever things. They can also be used as three different types of oscillators. (a) Astable Multivibrator - constantly oscillates For frequencies above 1 cycle per second, it is called an oscillator (multivibrator or square wave oscillator). For frequencies below 1 cycle per second it is called a TIMER or DELAY. (b) Monostable - changes state only once per trigger pulse - also called a ONE SHOT (c) Voltage Controlled Oscillator - called a VCO.

to Index

THE ASTABLE (or FREE RUNNING) MULTIVIBRATOR The capacitor C charges via R1 and R2 and when the voltage on the capacitor reaches 2/3 of the supply, pin 6 detects this and pin 7 connects to 0v. The capacitor discharges through R2 until its voltage is 1/3 of the supply and pin 2 detects this and turns off pin 7 to repeat the cycle. The top resistor is included to prevent pin 7 being damaged as it shorts to 0v when pin 6 detects 2/3 rail voltage. Its resistance is small compared to R2 and does not come into the timing of the oscillator. The following graph applies to the Astable circuit: Using the graph: Suppose R1 = 1k, R2 = 10k and C = 0.1 (100n). Using the formula on the graph, the total resistance = 1 + 10 + 10 = 21k The scales on the graph are logarithmic so that 21k is approximately near the "1" on the 10k. Draw a line parallel to the lines on the graph and where it crosses the 0.1u line, is the answer. The result is approx 900Hz. Suppose R1 = 10k, R2 = 100k and C = 1u Using the formula on the graph, the total resistance = 10 + 100 + 100 = 210k The scales on the graph are logarithmic so that 210k is approximately near the first "0" on the 100k. Draw a line parallel to the lines on the graph and where it crosses the 1u line, is the answer. The result is approx 9Hz. The frequency of an astable circuit can also be worked out from the following formula: frequency = 1.4 (R1 + 2R2) × C 555 astable frequencies C R1 = 1k R2 = 6k8 R1 = 10k R2 = 68k R1 = 100k R2 = 680k 0.001µ 100kHz 10kHz 1kHz 0.01µ 10kHz 1kHz 100Hz 0.1µ 1kHz 100Hz 10Hz 1µ 100Hz 10Hz 1Hz 10µ 10Hz 1Hz 0.1Hz

to Index

HIGH FREQUENCY OSCILLATORS 360kHz is the absolute maximum as the 555 starts to malfunction with irregular bursts of pulses above this frequency. To improve the performance of the oscillator, a 270R and 1n can be added as shown in the second circuit:

to Index

LOW FREQUENCY OSCILLATORS - called TIMERS If the capacitor is replaced with an electrolytic, the frequency of oscillation will reduce. When the frequency is less than 1Hz, the oscillator circuit is called a timer or "delay circuit." The 555 will produce delays as long as 30 minutes but with long delays, the timing is not accurate. 555 Delay Times: C R1 = 100k R2 = 100k R1 = 470k R2 = 470k R1 = 1M R2 = 1M 10µ 2.2sec 10sec 22sec 100µ 22sec 100sec 220sec 470µ 100sec 500sec 1000sec The following circuits show a 1-5 minute timer and 10 minute timer:

to Index

SQUARE WAVE OSCILLATOR KIT: A square wave oscillator kit can be purchased from Talking Electronics for approx $10.00 See website: Square Wave Oscillator It has adjustable (and settable) frequencies from 1Hz to 100kHz and is an ideal piece of Test Equipment. Buy a kit (This link will send an email to Colin Mitchell and you will be advised of costs and how to send money via Paypal or credit card.)

to Index

Monostable or "One Shot" or Pulse Extender When the circuit is turned on, the output is LOW and a brief negative pulse on pin 2 will make the output go HIGH for a period of time determined by the value of R and C. If pin 2 is low for longer than this period, the output will remain HIGH while pin 2 is LOW and immediately go LOW when pin 2 goes HIGH. CIRCUIT OPERATION When the circuit is turned on, the capacitor is uncharged. Pin 6 sees a LOW and pin 2 sees a HIGH. Remember: Pin 2 must be LOW to make the output HIGH. Pin 6 must be HIGH to make the output LOW. Neither pin is "controlling the chip" at start-up and the chip is designed to output a LOW with these start-up conditions. In other words, the chip starts in RESET mode. Pin 7 is LOW and the capacitor does not charge. When pin 2 see a LOW pulse, the chip goes to SET mode and the output goes HIGH. Pin 7 goes OPEN and capacitor C charges via R. When pin 6 sees 2/3 rail voltage, the chip goes to RESET mode with pin 3 and 7 LOW. The capacitor instantly discharges and the circuit waits for a negative pulse on pin 2.

to Index

"No-No's" Here are 4 mistakes to avoid: 1. Pin 7 gets connected to the 0v rail via a transistor inside the chip during part of the operation of the 555. If the pot is turned to very low resistance in the following circuit, a high current will flow through the pot and it will be damaged: 2. The impedance of the 100u electrolytic will allow a very high current to flow and the chip will get very hot. Use 10u maximum when using 8R speaker. 3. The reset pin (pin 4) is internally tied HIGH via approx 100k but it should not be left floating as stray pulses may reset the chip. 4. Do not draw 555 circuits as shown in the following diagram. Keep to a standard layout so the circuit is easy to follow.

to Index

REPLACING A 556 WITH TWO 555's Here is a handy reference to replace a 556 dual timer with two 555's:

to Index

SUBSTITUTING A 555 - part 1 Although a 555 is a wonderful chip, it may not be the best choice for some applications. You may require an oscillator frequency higher than 1MHz, or a very low quiescent current, or have some gates available in other chips. You may also need 4 or more 555's to get the timing and delays you require. Here are some circuits to help you substitute a 555. The 74c14 IC contains 6 Schmitt Trigger gates and each gate can be used to replace a 555 in SOME circuits. The voltage for a 4c14 is 3v to 15v. Maximum output current per gate is 15mA. Max frequency of operation: 2MHz - 5MHz. Quiescent current is 1uA if all inputs are 0v or rail voltage.

to Index

SUBSTITUTING A 555 - part 2 If you need a special function or special effect, it may take 2, 3 or more 555's to do the job. The 74c14 has 6 gates and can create 6 "building blocks." Here are some circuits to show its versatility: 2 MINUTE TIMER The relay is energized for a short time, 2 minutes after the push-button is pressed. The push-button produces a brief LOW on pin 1, no matter how long it is pushed and this produces a pulse of constant length via the three components between pin 2 and 3. This pulse is long enough to fully discharge the 100u timing electrolytic on pin 5. The 100k and electrolytic between pins 6 and 9 are designed to produce a brief pulse to energize the relay. OUTPUT AFTER 2 MINUTES Here is another very similar circuit. Use either the active HIGH or Active LOW switch and if the Active LOW switch is used, do not connect the parts or gate between pins 1 and 2 to the rest of the circuit. PULSER The 74c14 can be used for lots of different circuits. In the following design, the output produces 3mS pulses every second. The circuit is adjustable to a wide range of requirements. TRIGGER TIMER The next design interfaces a "Normally Open" and "Normally Closed" switch to a delay circuit. The feedback diode from the output prevents the inputs re-triggering the timer (during the delay period) so that a device such as a motor, globe or voice chip can be activated for a set period of time.

to Index

BUILDING THE CIRCUITS The fastest way to put a circuit together is on BREADBOARD. The cheapest and best bread-board has power-rails and sets of "tie-points" or "holes" as shown in this photo: Connect the components with hook-up wire by stripping the ends to expose the wire at both ends. Or you can use 0.5mm tinned copper wire (make sure the jumpers do not touch each other). Do not cut the leads of the components as you may want long leads on another project. Neatness is not important. The important thing is to build as many circuits as possible as each one will help you understand how the 555 works and how the external circuitry modifies the signal to produce the resulting effect. There is a point-to-learn in every circuit.

PROJECTS
                 to Index

TOY ORGAN This circuit produces a tone according to the button being pressed. Only 1 button can be pressed at a time, that's why it is called a monophonic organ.

to Index

TICKING BOMB This circuit sound just like a ticking bomb.

to Index

METAL DETECTOR This circuit detects metal and also magnets. When a magnet is brought close to the 10mH choke, the output frequency changes.

to Index

UNEVEN CLICKS This circuit produces two clicks then a short space before two more clicks etc. Changing the voltage on pin, 5 via the diode, adjusts the timing of the chip.

to Index

FLASHING RAILROAD LIGHTS This circuit flashes two red LEDs for a model railway crossing.

to Index

SCREAMER This circuit will produce an ear-piercing scream, depending on the amount of light being detected by the Light Dependent Resistor.

to Index

LASER RAY This circuit produces a weird "Laser Ray" sound and flashes a white LED at approx 5Hz:

to Index

LED DIMMER This circuit will adjust the brightness of one or more LEDs from 5% to 95%.

to Index

MOTOR PWM The speed of a motor can be adjusted by this circuit, from 5% to 95%.

to Index

VOLTAGE DOUBLER A voltage higher than the supply can be created by a "Charge-Pump" circuit created with a 555, diodes and capacitors as shown in the following circuit. The output will deliver about 50mA

to Index

NEGATIVE VOLTAGE A negative supply can be produced by a "Charge-Pump" circuit created with a 555, diodes and capacitors as shown in the following circuit. The output will deliver about 50mA.

to Index

555 AMPLIFIER The 555 can be used as an amplifier. It operates very similar to pulse-width modulation. The component values cause the 555 to oscillate at approx 66kHz and the speaker does not respond to this high frequency. Instead it responds to the average CD value of the modulated output and demonstrates the concept of pulse-width modulation. The chip gets very hot and is only for brief demonstrations.

to Index

LIGHT DETECTOR This circuit detects light falling on the Photo-cell (Light Dependent Resistor) to turn on the 555 and create a tone that is delivered to the speaker. Pin 4 must be held below 0.7v to turn the 555 off. Any voltage above 0.7v will activate the circuit. The adjustable sensitivity control is needed to set the level at which the circuit is activated. When the sensitivity pot is turned so that it has the lowest resistance (as shown in red), a large amount of light must be detected by the LDR for its resistance to be low. This produces a voltage-divider made up of the LDR and 4k7 resistor. As the resistance of the LDR decreases, the voltage across the 4k7 increases and the circuit is activated. When the sensitivity control is taken to the 0v rail, its resistance increases and this effectively adds resistance to the 4k7. The lower-part of the voltage-divider now has a larger resistance and this is in series with the LDR. Less light is needed on the LDR for it to raise the voltage on pin 4 to turn the 555 on.

to Index

DARK DETECTOR When the level of light on the photo-cell decreases, the 555 is activated. Photo-cells (Photo-resistors) have a wide range of specifications. Some cells go down to 100R in full sunlight while others only go down to 1k. Some have a HIGH resistance of between 1M and others are 10M in total darkness. For this circuit, the LOW resistance (the resistance in sunlight) is the critical value. More accurately, the value for a particular level of illumination, is the critical factor. The sensitivity pot adjusts the level at which the circuit turns on and allows almost any type of photo-cell to be used.

to Index

FLIP FLOP and MEMORY CELL When output pin 3 is HIGH, the 220n charges through the 220k to 6v. When pin 3 is LOW, the 220n discharges through the 220k to 0v. Pressing the switch upsets the 3v created by the two 10k voltage dividers, triggering the flip flop inside the 555 and changing the state of the output from HIGH to LOW or vice-versa. The output of the 555 drives a transistor to turn a globe on and off. The second circuit is a Memory cell and is the basis of the memory in a computer. The SET button turns on the globe and the RESET button turns the globe off.

to Index

CAR TACHOMETER A 555 is configured as a monostable or one shot in this project. The period of the 555 is determined by the 47k and the capacitor from pin 6 to ground (100n). Time "T" = 1.1 RC or 1.1 X 50,000 X 0.1 X10 -6 = 0.0055 or 5.5 mS (milli-seconds). The 555 receives trigger pulses from the distributor points. These are limited by the 1k and 5v zener diode. These are AC coupled to the trigger input through the 100n coupling capacitor. The 50mA meter receives pulses of current through the 200k pot to show a reading. Integration of the current pulses produces a visible indication of the cars engine speed on the 0-1mA meter. Supply is taken from the cars 12v system and for the 555 it is reduced to a regulated 9v by the 15 ohm resistor in conjunction with the 9v zener diode. Note: the 10u electrolytic must be placed physically as close as possible to supply pin 8.

to Index

SERVO TESTER This circuit can be used to manually turn a servo clockwise and anti-clockwise. By pushing the forward or reverse button for a short period of time you can control the rotation of the servo. It will also test a servo.

to Index

TRANSISTOR TESTER The 555 operates at 2Hz. Output pin 3 drives the circuit with a positive then zero voltage. The other end of the circuit is connected to a voltage divider with the mid-point at approx 4.5v. This allows the red and green LEDs to alternately flash when no transistor is connected to the tester. If a good transistor is connected, it will produce a short across the LED pair when the voltage is in one direction and only one LED will flash. If the transistor is open, both LED’s will flash and if the transistor is shorted, neither LED will flash.

to Index

SWITCH DEBOUNCE The output goes HIGH for 100mS when the switch is pressed.

to Index

INCREASING OUTPUT CURRENT The 555 will deliver 200mA to a load but the chip gets extremely hot (12v supply). The answer is to use a buffer transistor. For 200mA, use a BC547 or equivalent. For 500mA use a BC337 or equivalent For 1A, use a TIP31 or equivalent. For 3A - 5A use a BD679 or equivalent with heatsink For 5A to 10A use TIP3055 with heatsink

to Index

INCREASING OUTPUT PUSH-PULL CURRENT Some 555's do not swing rail-to-rail when 200mA is being delivered and the chip gets very hot when trying to deliver 200mA. The solution is to add a push-pull output. The following arrangement has been chosen as it swings almost rail-to-rail but two faults need to be addressed. Both transistors turn on during the brief interval when pin 3 is travelling from high to low or low to high. This means the two transistors will put a "short" across the power rail. The addition of the 4R4 will allow a high current to flow but the transistors will not be damaged. In addition, diodes on the base of each transistor allows alternate ones to turn off when output pin 3 is HIGH or LOW.

to Index

DRIVING A BI-COLOUR LED Some 3-leaded LEDs produce red and green. This circuit alternately flashes a red/green bi-coloured LED:

to Index

BI-POLAR LED DRIVER Some 2-leaded LEDs produce red and green. These are called Bi-polar LEDs. This circuit alternately flashes a red/green bi-polar LED:

to Index

ZENER DIODE TESTER This circuit will test zener diodes up to 56v. See Talking Electronics website, left index, 200 Transistor Circuits (circuits 1-100) and go to Zener Diode (making) to see how to make a zener diode and how to create a zener voltage from a combination of zeners. Place the zener across the terminals in the circuit below and read the value across it with a multimeter set to 50v range.

to Index

WAILING SIREN By pressing the button, the wailing sound increases. Releasing the button decreases the wailing. The circuit automatically turns off after about 30 seconds.

to Index

CONTINUITY TESTER This circuit will detect low resistances and high resistances to produce a tone from the speaker. It will detect up to 200k and the circuit automatically turns off when the probes are not used.

to Index

MORSE KEYER This circuit will help you master the art of keying Morse Code:

to Index

STUN GUN This circuit produces a very high voltage and care must be used to prevent getting a nasty shock. The transformer can produce over 1,000v and the 8-stage multiplier can produce up to 20,000v

to Index

12v to 240v INVERTER This circuit will produce 240v at 50Hz. The wattage will depend on the driver transistors and transformer.

to Index

ACTIVE LOW TRIGGER This circuit sits LOW and the output goes HIGH when the push-button is pressed. When the normally-closed push button is pressed, it opens and the uncharged 1u will be pulled to nearly 0v rail via the 10k and this will take pin 2 LOW to make output pin 3 HIGH for the duration determined by the 22u and 100k. If the push-switch stays open, the 1u will charge via the 100k and eventually the output of the 555 will go low. But normally the switch must be pressed for a short period of time so that the timing components (100k and 22u) make the output go HIGH for a short period of time. This circuit is called an ACTIVE LOW TRIGGER

to Index

ACTIVE HIGH TRIGGER This circuit produces a HIGH output via a HIGH trigger:

to Index

MACHINE GUN This circuit produces a sound very similar to a machine gun:

to Index

LATCH This circuit is a LATCH and remains ACTIVE when the push-button has been pressed for an INSTANT and released.

to Index

KNIGHT RIDER In the Knight Rider circuit, the 555 is wired as an oscillator. It can be adjusted to give the desired speed for the display. The output of the 555 is directly connected to the input of a Johnson Counter (CD 4017). The input of the counter is called the CLOCK line. The 10 outputs Q0 to Q9 become active, one at a time, on the rising edge of the waveform from the 555. Each output can deliver about 20mA but a LED should not be connected to the output without a current-limiting resistor (330R in the circuit above). The first 6 outputs of the chip are connected directly to the 6 LEDs and these "move" across the display. The next 4 outputs move the effect in the opposite direction and the cycle repeats. The animation above shows how the effect appears on the display. Using six 3mm LEDs, the display can be placed in the front of a model car to give a very realistic effect. The same outputs can be taken to driver transistors to produce a larger version of the display. The Knight Rider circuit is available as a kit for less than $15.00 plus postage as Kitt Scanner. Buy Kitt Scanner kit Here is a simple Knight Rider circuit using resistors to drive the LEDs. This circuit consumes 22mA while only delivering 7mA to each LED. The outputs are "fighting" each other via the 100R resistors (except outputs Q0 and Q5).

to Index

FLASHING INDICATORS This is a request from Daniel, one of our subscribers. He needed to flash "turn indicators" using a 555 and a single 20 amp relay. Here is our suggestion. The timing resistor needs to be selected for the appropriate flash-rate. Flashing the "TURN INDICATORS"

to Index

TOUCH SWITCH The Touch Switch circuit will detect stray voltages produced by mains voltages and electrostatic build-up in a room. Pin 2 must see a LOW for the circuit to activate. If sufficient static voltage is detected by the plate, the chip will change state. If not, you will need to touch the plate and the 0v rail. The circuit can be made 100 times more sensitive by adding a transistor to the front-end as shown in the diagram below:

to Index

SIREN 100dB This is a very loud siren and if two or more piezo's are located in a room, the burglar does not know where the sound is coming from. A robber will not stay anywhere with an ear-piercing sound as he cannot hear if someone is approaching. It's the best deterrent you can get. The "F" contact on the piezo is "feedback" and is not needed in this circuit.

to Index

POLICE SIREN The Police Siren circuit uses two 555's to produce an up-down wailing sound. The first 555 is wired as a low-frequency oscillator to control the VOLTAGE CONTROL pin 5 of the second 555. The voltage shift on pin 5 causes the frequency of the second oscillator to rise and fall.

to Index

HEE HAW SIREN Build the circuit and listen. Change the resistors and capacitors to get all sorts of different results.

to Index

RAIN ALARM This circuit consumes no current until moisture is detected on the rain plate.

to Index

PWM CONTROLLER This controller will deliver up to 30 amps and control the motor from 5% to 95%.

to Index

HULDA CLARK ZAPPER This is the circuit for Dr. Hulda Clark's Zapper, designed in 2003. The frequency is approximately 30kHz positive offset square wave. It has a red LED light that lights up when the unit is on. Perfect for regular zapping, extended zapping and other Hulda Clark related experiments. This device is used to cure, treat and prevent any disease. It will cure anything. Simply hold the two probes (one in each hand) for 5-10 minutes then rest for 20 minutes, then repeat two more times. Do this each day and you will be cured. Here is the .pdf of her book: A Cure For All Diseases. Website: http://clarktestimonials.com/ Hundreds of people have been cured of everything from herpes to AIDS.

to Index

TILT SWITCH The output is LOW at start-up due to the capacitor on pin 4. When the mercury switch closes, the output goes HIGH and remains HIGH until the reset button is pressed. This circuit is called a LATCH. See Latch circuit and Memory Cell above.

to Index

MOSQUITO REPELLENT This circuit produces a tone above the human audible range and this is supposed to keep the mosquitoes away.

to Index

DRIVING A RELAY The 555 will activate a relay. When pins 2 and 6 are connected as an input, the chip requires only about 1uA to activate the output. This is equivalent to a gain of about 200,000,000 (200 million) and represents about 4 stages of amplification via transistors. In the first circuit, the output will be opposite to the input. The relay can be connected "high" or "low" as show in the second diagram. One point to note: The input must be higher than 2/3V for the output to be low and below 1/3V for the output to be high. This is called HYSTERESIS and prevents any noise on the input creating "relay chatter." NEGATIVE LOGIC An interesting point to remember. In the first diagram above, the relay is connected so that it is active when the output is low. This is called NEGATIVE or NEGATIVE LOGIC. It has the same reasoning as -5 - (-5) = 0. Or in English: "I am not NOT going." When the input is low in the first diagram, the output is HIGH and the relay is OFF. The circuitry creates two reversals and makes it easy to see that when the input is LOW, the relay is OFF.

to Index

SCHMITT TRIGGER (Hysteresis) This circuit is the same as Driving A Relay circuit above. It is the same circuit with a different name. We have also animated the circuit to show how the output goes high or low according to the input level. The animation shows a wide gap between the input levels when the time when the output goes HIGH or LOW and this gap is called the HYSTERESIS GAP. This circuit is called a SCHMITT TRIGGER and it is used in many building-blocks to prevent false triggering. It prevents false triggering because as the input rises, the output does not change until the input voltage is fairly high. If the input voltage falls, the output does not change until the input falls about 30%. This means small fluctuations (noise) on the input do not have any effect on the output. The output is the INVERSE of the input - in other words the 555 is a SCHMITT INVERTER.

to Index

MUSIC BOX This circuit produces 10 different tones and by selecting suitable values to change the voltage on pin 5, the result can be quite pleasing. Note: the two unused outputs of the 4017 produce a tone equal to that produced by the 555 when pin 5 has no external control voltage.

to Index

REACTION TIMER GAME This is a game for two players. Player 1 presses the START button. This resets the 4026 counter chip and starts the 555 oscillator. The 555 produces 10 pulses per second and these are counted by the 4026 chip and displayed on the 7-Segment display. The second player is required to press the STOP button. This freezes the display by activating the Clock Inhibit line of the 4026 (pin 2). Two time-delay circuits are included. The first activates the 555 by charging a 10u electrolytic and at the same time delivering a (high) pulse to the 4026 chip to reset it. The second timer freezes the count on the display (by raising the voltage on pin 2) so it can be read.

to Index

TRAFFIC LIGHTS Here's a clever circuit using two 555's to produce a set of traffic lights for a model layout. The animation shows the lighting sequence and this follows the Australian-standard. The red LED has an equal on-off period and when it is off, the first 555 delivers power to the second 555. This illuminates the Green LED and then the second 555 changes state to turn off the Green LED and turn on the Orange LED for a short period of time before the first 555 changes state to turn off the second 555 and turn on the red LED. A supply voltage of 9v to 12v is needed because the second 555 receives a supply of about 2v less than rail. This circuit also shows how to connect LEDs high and low to a 555 and also turn off the 555 by controlling the supply to pin 8. Connecting the LEDs high and low to pin 3 will not work and since pin 7 is in phase with pin 3, it can be used to advantage in this design.

to Index

DRIVING MANY LEDS The 555 is capable of sinking and sourcing up to 200mA, but it gets very hot when doing this on a 12v supply. The following circuit shows the maximum number of white LEDs that can be realistically driven from a 555 and we have limited the total current to about 130mA as each LED is designed to pass about 17mA to 22mA maximum. A white LED drops a characteristic 3.2v to 3.6v and this means only 3 LEDs can be placed in series.

to Index

TV REMOTE CONTROL JAMMER This circuit confuses the infra-red receiver in a TV. It produces a constant signal that interferes with the signal from a remote control and prevents the TV detecting a channel-change or any other command. This allows you to watch your own program without anyone changing the channel !! The circuit is adjusted to produce a 38kHz signal. The IR diode is called an Infra-red transmitting Diode or IR emitter diode to distinguish it from a receiving diode, called an IR receiver or IR receiving diode. (A Photo diode is a receiving diode). There are so many IR emitters that we cannot put a generic number on the circuit to represent the type of diode. Some types include: CY85G, LD271, CQY37N (45¢), INF3850, INF3880, INF3940 (30¢). The current through the IR LED is limited to 100mA by the inclusion of the two 1N4148 diodes, as these form a constant-current arrangement when combined with the transistor and 5R6 resistor.

to Index

3x3x3 CUBE This circuit drives a 3x3x3 cube consisting of 27 white LEDs. The 4020 IC is a 14 stage binary counter and we have used 9 outputs. Each output drives 3 white LEDs in series and we have omitted a dropper resistor as the chip can only deliver a maximum of 15mA per output. The 4020 produces 512 different patterns before the sequence repeats and you have to build the project to see the effects it produces on the 3D cube.

to Index

UP/DOWN FADING LED This circuit makes the LED fade on and off by charging the 100u. The transistor amplifies the current entering the 100u and delivers 100 times this value to the LED via the collector-emitter pins. The circuit needs 9v for operation since pin 2 of the 555 detects 2/3Vcc before changing the state of the output so we only have a maximum of 5.5v via a 220R resistor to illuminate the LED.

to Index

555 KIT Buy 555 kit Or email Colin Mitchell: talking@tpg.com.au A kit of components to make many of the circuits described in this eBook is available for $10.00 plus $7.00 post. The kit contains the following components: 2 - 220R 2 - 1k 2 - 4k7 2 - 10k 2 - 33k 2- 100k 2 - 1M 1 - 10k mini pot 1 - 100k mini pot 2 - 10n 2 - 100n 1 - 10u electrolytic 1- 100u electrolytic 2 - 1N4148 signal diodes 2 - BC547 transistors 1 - BC557 transistor 1 - 555 timer chip 1 - 8 pin IC socket 1 - red LED 1 - green LED 1 - orange LED 1 - mini 8R speaker 1 - mini piezo 1 - LDR (Light Dependent Resistor) 1 - 10mH inductor 1 - push button 1 - tactile push button 1 - Experimenter Board (will take 8, 14 and 16 pin chips)

to Index

not copyright   29-11-2009  Colin Mitchell    You can copy and use anything.